## Slide 1
 | List Price | Reagent costs/run | Reagent costs/Mb | Error rates (%) | Run Time | Millions of Reads/run | Bases/read | MB/run | BACs,plastids, microbial genomes | Transcriptome | Plant/Animal genomes | Metagenomics | Mutation Detection | Comments
3730xl (capillary) | $376k | $144 | $2,308 | 0.1-1 | 2 hrs | 9.6x10-5 | 650 | 0.06 |  |  |  |  |  | 
454 GS Jr. | $108k | $1,100 | $22 | 1 | 10 hrs | 0.1 | 400 | 50 | Good; expensive | Need many runs; expensive | Way too expensive | Costs limit sample # and depth | Way too expensive | 
454 FLX Ti | $450k | $6,200 | $12 | 1 | 10 hrs | 1 | 400 | 400 | Good; should multiplex | Good; expensive | Not for use alone | Good but expensive | Expensive; good for identifying clusters | Reliability issues
PacBio RS | $695k | $~300 | $2-17 | <1 | <2 hrs | 0.03 | >3,000 | 100-150 | Good for hybrid assemblies | Good for hybrid assemblies | Good for hybrid assemblies and mixed platform strategy | Expensive but long reads good for hybrid sequencing | Way too expensive; insufficient accuracy | Not evolving as quickly as other platforms
Ion Torrent | $49k | $539-939 | $5-0.60 | ~1 | 4-7 hrs | 0.1-4 | 400 | 40-1,500 | Less data than MiSeq | Reads similar to 454 but less expensive | Less $ than 454, more than Proton or Illumina | Commonly replacing 454 | More $ than MiSeq, HiSeq, SOLid, Proton | $ increasing with increased read length
Ion Torrent Proton I | $224k | $1,050 | $0.09 | ~1 | <4 hrs | 70 | <200 | 10,000 | More data than needed; assembly challenge | Assembly even more challenging than Illumina | Expensive compared to HiSeq or Proton II/III | Shorter reads than 454 or MiSeq; longer than HiSeq | More $ than HiSeq or SOLid | 
SOLiD | $251k | $10,503 | $0.07 | <0.1 | 8 days | >1,410 | 75+35 | 155,100 | More data than needed; assembly challenge | Super short reads make assembly verge near impossible | Super short reads make assembly verge near impossible | Reads too short | Common platform used | Being replaced by better technology
MiSeq v2 | $125k | $1,040 | $0.70 | ~0.1 | 39 hrs | 15 | 250+250 | 7,500 | Good; should multiplex | Expensive; reads longer | Expensive; reads longer | Good; shorter reads than 454 but more depth | More expensive than HiSeq, SOLiD or Proton II | Kits are expensive
GAIIx | $250k | $17,575 | $0.19 | ~0.1 | 14 days | 300 | 150+150 | 96,000 |  |  |  |  |  | 
HiSeq 1000 | $560k | $10,220 | $0.04 | ~0.1 | 8.5 days | <1,500 | 100+100 | <300,000 |  |  |  |  |  | 
HiSeq 2000 | $690k | $23,470 | $0.04 | ~0.1 | 11.5 days | <3,000 | 100+100 | <600,000 | More data than needed; assembly challenge | Good; assembly challenge; more data | Primary platform used | Good; short reads | Common platform used | 
HiSeq 2500 | $690k | $6,145 | $0.05 | ~0.1 | 40 hrs | <600 | 150+150 | <180,000 | More data than needed; assembly challenge | Good; assembly challenge; more data | Primary platform used | Good; short reads | Common platform used | 

## Slide 2
 | List Price | Reagent costs/run | Reagent costs/Mb | Error rates (%) | Run Time | Millions of Reads/run | Bases/read | MB/run | BACs, plastids, microbial genomes | Transcriptome | Plant/Animal genomes | Metagenomics | Mutation Detection | Comments
HiSeq 2500 rapid run | $690k? My guess | 6,145 | 0.05 | ~0.1 | 40 hrs | <600 | 150+ 150 | <180,000 | More data than need; assembly challenge | Good; lots of data; assembly challenge | More $ than HiSeq2000 but inc. read length | Good but limited by short reads | Common platform | Unknown reagents costs
Ion Torrent Proton II | $224k | 1,000 | 0.02 | 1 | >4 hrs | 250 | <200 | 50,000 | More data than needed; assembly challenge | Assembly worse than Illumina | Similar to HiSeq | Longer reads than HiSeq | Similar cost to HiSeq and SOLiD | >400 bp reads!
Ion Torrent Proton III | $224k | 1,000 | 0.01 | 1 | >4 hrs | 500 | <200 | 100,000 | More data than needed | Need assembly pipelines | Best based on $/MB | Longer reads than HiSeq | Projected to be cost leader | >400 bp reads!
minION | $0 | <900 | 1 | 4 | <6 hrs | 0.1 | 9,000 | 1,000 | More expensive than GridION | More expensive than GridION | More expensive than GridION | Good for env samples, FIELD PORTABLE! but limited by accuracy | Accuracy limiting factor | Unknown availability date
GridION | 30? | Varies | 0.04 | 4 | ? | 5 | 10,000 | 100,000 | High error rate; great for combining platforms | High error rate; great for combining platforms | High error rate; great for combining platforms | Good for env samples, limited by accuracy | Accuracy limiting factor | Unknown availability date; reagents $ unknown